## Slide 1
CEPS Engineering Organization
Welding
University of New Hampshire
Students for the Exploration and Development of Space

## Slide 2: Tungsten inert gas welding (tig)
University of New Hampshire
Students for the Exploration and Development of Space

## Slide 3
University of New Hampshire
Students for the Exploration and Development of Space
Background
What is TIG?
  Tungsten Inert Gas
Also referred to as GTAW
  Gas Shielded Tungsten Welding
In TIG welding, a tungsten electrode heats the metal you are welding and gas (most typically Argon) protects the weld from airborne contaminants

## Slide 4
University of New Hampshire
Students for the Exploration and Development of Space
Background
TIG welding uses a non-consumable tungsten
Filler metal, when required, is added by hand
Shielding gas protects the weld and tungsten

## Slide 5
University of New Hampshire
Students for the Exploration and Development of Space
Advantages
Welds more metals and metal alloys than any other process
High quality and precision
Aesthetic weld beads
No sparks or spatter
No flux or slag
No smoke or fumes

## Slide 6
University of New Hampshire
Students for the Exploration and Development of Space
Lower filler metal deposition rates
Good hand-eye coordination a required skill
Brighter UV rays than other processes
Slower travel speeds than other processes
Equipment costs tend to be higher than other processes
Disadvantages

## Slide 7
University of New Hampshire
Students for the Exploration and Development of Space
Safety
Electric shock can kill.
  Always wear dry insulating gloves
  Insulate yourself from work and ground
  Do not touch live electrical parts
  Keep all panels and covers securely in place
Fumes and gases can be hazardous to your health.
  Keep your head out of the fumes
  Ventilate area, or use breathing device

## Slide 8
University of New Hampshire
Students for the Exploration and Development of Space
Safety
Welding can cause fire or explosion.
  Do not weld near flammable material
  Watch for fire; keep extinguisher nearby
  Do not locate unit over combustible surfaces
  Do not weld on closed containers
Arc rays can burn eyes and skin; Noise can damage hearing.
  Wear welding helmet with correct shade of filter
  Wear correct eye, ear, and body protection

## Slide 9
University of New Hampshire
Students for the Exploration and Development of Space
Safety
Hot parts can cause injury.
  Allow cooling period before touching welded metal
  Wear protective gloves and clothing
Magnetic fields from high currents can affect pacemaker operation.
Flying metal can injure eyes.
  Welding, chipping, wire brushing, and grinding cause sparks and flying metal; wear approved safety glasses with side shields

## Slide 10
University of New Hampshire
Students for the Exploration and Development of Space
Types of Weld Joints
Each one include different overall techniques for laying beautiful beads
All the advice you would need can be found with a simple google search

## Slide 11
University of New Hampshire
Students for the Exploration and Development of Space
Our Shop - Overview

## Slide 12
University of New Hampshire
Students for the Exploration and Development of Space
Our Shop - Preparation
There is no such thing as TOO clean!
The Tig Torch
The Tig Torch
Turn on Argon Flow
Starts when Tig Welding starts
Ground the Worktable

## Slide 13
University of New Hampshire
Students for the Exploration and Development of Space
Our Shop – Final Checks
Select the right filler (material, thickness)
Select the right settings on the machine
Amperage
AC/DC
etc
Make sure torch is good to go
Get pedal in a comfortable spot

## Slide 14
University of New Hampshire
Students for the Exploration and Development of Space
Our Shop – ENSURE PPE
Jacket
Helmet (power on)
Gloves

## Slide 15
University of New Hampshire
Students for the Exploration and Development of Space
Example of Welding

## Slide 16
University of New Hampshire
Students for the Exploration and Development of Space
The Future of Welding
Humans are too imperfect
Robots can ensure the same thing happens every time…
Cough…starship…cough

## Slide 17
University of New Hampshire
Students for the Exploration and Development of Space
Welding Parameters
Aluminum weld parameters

## Slide 18
University of New Hampshire
Students for the Exploration and Development of Space
Welding Parameters
Stainless steel weld parameters

## Slide 19
University of New Hampshire
Students for the Exploration and Development of Space
Welding Parameters
Mild steel weld parameters

## Slide 20
University of New Hampshire
Students for the Exploration and Development of Space
Electrode Selection

## Slide 21
University of New Hampshire
Students for the Exploration and Development of Space
Apps
Pocket Welder Helper
Miller Welding
Helps you select the right settings and equipment for a particular weld job